Vproc register map:
(vproc0: 0xb0004000, vproc1:0xb0003000, vproc2:0xb0008000, vproc3:0xb0002000, vproc4:0xb0006000)
	Addr offset
.id	0x00	8 bits	bit7-bit6: soc No / bit5-bit3: video in No / bit2-bit0: video out No
.enable	0x04	16 bits	(0: disable 1: enable) / Bit0: video out 0 enable / bit1: video out 1 enable / bit2: video out 2 enable / bit3: video out 3 enable / bit4: video out 4 enable / bit5: video out 5 enable / bit6: video out 6 enable / bit7: video out 7 enable / bit8: video out 0 flip enable / bit9: video out 1 flip enable / bit10: video out 2 flip enable / bit11: video out 3 flip enable / bit12: video out 4 flip enable / bit13: video out 5 flip enable / bit14: video out 6 flip enable / bit15: video out 7 flip enable
.zoom0	0x10	32bits	Video out 0: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1
.zoom1	0x14	32bits	Video out 1: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1
.zoom2	0x18	32bits	Video out 2: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1
.zoom3	0x1c	32bits	Video out 3: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1
.zoom4	0x20	32bits	Video out 4: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1
.zoom5	0x24	32bits	Video out 5: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1
.zoom6	0x28	32bits	Video out 6: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1
.zoom7	0x2c	32bits	Video out 7: zoom paramter. / Bit15 – bit0: coloumn zoom / (1920 – col) * 65535 /1920+1 / bit31 – bit16: raw zoom / (1080 – raw) *65535/ 1080+1

Sout register Map:
(sout0: sout <0xb0001000>, mix <0xb00e0000>, dma <0xb00c0000>)
	Addr offset
buffer0_addrl	0x100	32bits
buffer0_addrh	0x104	32bits
buffer1_addrl	0x108	32bits
buffer1_addrh	0x10c	32bits
buffer2_addrl	0x110	32bits
buffer2_addrh	0x114	32bits
buffer3_addrl	0x118	32bits
buffer3_addrh	0x11c	32bits
Stride	0x120	32bits
Enable	0x124	32bits
Error	0x128	32bits

video(n)_offset	0x0000 + (n * 0x10)	32bits
video(n)_width	0x0004 + (n * 0x10)	16bits
video(n)_height	0x0006 + (n * 0x10)	16bits

Internal sync command protocol
SrcID	Guint16		M1:0x6d31(‘m1’) / m2:0x6d32(‘m2’) / m3:0x6d33(‘m3’) / m4:0x6d34(‘m4’)
desID	Guint16		M1:0x6d31(‘m1’) / m2:0x6d32(‘m2’) / m3:0x6d33(‘m3’) / m4:0x6d34(‘m4’)
Type	Guint8		0: ack / 1:heartbeat / 2:iddp / 3:vds0_setup / 4:vds1_setup / 5:key
Pkgno	Guint8
Len	guint16
Data	guint8[]

Protocol ‘data’
ack data:
Pkgno	Guint8
Status	Guint8		0:OK / 1: fault
Temperature	guint8
cpu_loading	guint8
mem_loading	guint8
Resv	guint8[3]
Sysbit	guint64

Iddp data:
iddp_mode	gint

vds0_setup/vds1_setup data
Same with part of data of STK protocol ‘Setup Video Frame’(<byte 16> to end).

Key data:
key	guint16

Key ack data:
ack data:
Pkgno	Guint8
Status	Guint8		Received key status
Temperature	guint8
cpu_loading	guint8
mem_loading	guint8
Resv	guint8[3]
Sysbit	guint64