SDK and system resources of B3VCU

Revision History
Name	Date	Reason For Changes	Version
Chen Yong	Jul 7, 2022	Initial draft	1.0.1
Chen Yong	Aug 3, 2022	Modify by VCU_IDS_V0.2.xlsx requirement	1.0.2

# Scope
# System

VCU
VDU
CAM
Display
RTP/UDP
player
Hub
VCU Control
computer
Programming
computer
Sdi output 1

RS422

SDI(1-10)

SDI output(2-8)

Ethernet 0-1

Ethernet 2

Usb debug serial port

RS422

Figure is the full system physical linking. The devices and linking for programming are in the dotted line box.

# Enviroment
## VCU
Defaut setting:
static IP (192.168.1.254)
- username: root
- password: root
The user can download and upload files to VCU with sftp client software.
The user can control the VCU with the serial port debug application(e.g: teraterm).
The user also can log in and control the VCU with putty or ssh.
## Programming computer
- This computer is for programming the software fo the VCU. The Ubuntu(20.04) is required and verified to work.
- This computer has the same subnet IP address with the VCU.
- The user need install the requirement software eg Filezilla(sftp client), GTKTerm(serial debug) or ssh for downloading, uploading and debugging the VCU files.
- The user run sdk.sh(from teamone) to install the sdk compiler.
- <your-sdk-dir>/environment-setup-cortexa72-cortexa53-xilinx-linux includes the enviroment setup for the compiler. The user need setup the enviroment of the compiler based on their SDK requirement.
# B3VCU system resources
## External interface
### CAM UART
This port is link to the TI camera for the NUC controlling.
Physcial link: TIA/EIA-422
Device name: /dev/ttySC0
working mode:Duplex
flow control: no
### VDU UART
This port is link to the VDU for the VDU switching command.
Format: TIA/EIA-422
Device name: /dev/ttySC1
working mode:Duplex
flow control: no
### Spare UART
Format: TIA-232
Device name: /dev/ttyPS1, /dev/ttySC2, /dev/ttySC3
working mode:Duplex
flow control: no
### Ethernet
10/100/1000 BASE-T
- Port 1(eth2): VCU control port. default static IP 192.168.1.254
- Port 2(eth0): VCU RTP video stream port. Default Static IP 192.168.6.254
- Port 3(eth1): VCU RTP video stream port. Default Static IP 192.168.7.254
### KeyPad
Key No	Gpio port	Key name	Linux code
KEY_DIN_1	<axi_gpio_0 0>	key1	KEY_1(2)	Trailer ?
KEY_DIN_2	<axi_gpio_0 1>	key2	KEY_2(3)	Reverse Gear
KEY_DIN_3	<axi_gpio_0 2>	key3	KEY_3(4)	Forward Gear
KEY_DIN_4	<axi_gpio_0 3>	key4	KEY_4(5)	TBD
KEY_DIN_5	<axi_gpio_0 4>	key5	KEY_5(6)	TBD
KEY_DIN_6	<axi_gpio_0 5>	key6	KEY_6(7)	TBD
KEY_DIN_7	<axi_gpio_0 6>	key7	KEY_7(8)	TBD
KEY_DIN_8	<axi_gpio_0 7>	key8	KEY_8(9)	TBD

### Digital GPIO Output
DO No	Linux GPIO No	Terminal	Description
DO1	492	IR	On/OFF IR
DO2	493	IR	On/OFF IR
DO3	494	TBD
DO4	495	TBD
DO5	496	TBD

### SDI Video Input
Device name: /dev/media6 (/dev/video0)
/dev/media7 (/dev/video1)
/dev/media8 (/dev/video2)
/dev/media9 (/dev/video3)
/dev/media0 (/dev/video4)
/dev/media1 (/dev/video5)
/dev/media2 (/dev/video6)
/dev/media3 (/dev/video7)
/dev/media4 (/dev/video8)
/dev/media5 (/dev/video9)
### SDI video Output
SDI0 output: frmbuf_rd --> mix -> uhdsdi_tx (‘mix’ can mix video and osd)
SDI1 – SDI7 output: frmbuf_rd->udhsdi_tx. (without osd funciton)
There is a device “sdi_anc_tx” in all output. It can embed timestamp into the SDI signal.
all devices refer to internal interface:
frmbuf_rd: refer to 4.2.2
mix: refer to 4.2.3
uhdsdi_tx: refer to 4.2.4
sdi_anc_tx: refer to 4.2.5
### LED
LED	Linux GPIO No	Description
Green	458	Normal Status
Red	459	BIT error

## Internal Interface
### I2C
device name: /dev/i2c-0
slave chip: mb85rc256vfp slave address: 0x50
description: log data storage
### frmbuf_rd
Address: sdi0(0xb02d0000) sdi1(0xb02f0000) sdi2(0xb0310000) sdi3(0xb0330000) sdi4(0xb03a0000) sdi5(0xb03c0000) sdi6(0xb03e0000) sdi7(0xb0400000)
Support Format: Y_UV10, Y_UV8
refer to document (pg278-v-frmbuf.pd) provided by Xilinx
### mix
Address: 0xb02e0000
Primary video format: YUV4:2:2 10bits
Overlay layer1 format: BGRA8
Maximum resolution: 1920x1080
refer to doucument (pg243-v-mix.pdf) provided by Xilinx
### uhdsdi_tx
    Address: sdi0(0xa0040000) sdi1(0xa0060000) sdi2(0xa0080000) sdi3(0xa00a0000) sdi4(0xa0100000) sdi5(0xa0120000) sdi6(0xa0140000) sdi7(0xa0160000)
    Mode: 3G SDI 10bits
    format: NV16_10LE32
    refer to document (pg289-v-smpte-uhdsdi-tx-ss.pdf) provided by Xilinx
### sdi_anc_tx
    Address: sdi0(0xa01c0000) sdi1(0xa01d0000) sdi2(0xa01e0000) sdi3(0xa01f0000) sdi4(0xa0200000) sdi5(0xa0210000) sdi6(0xa0220000) sdi7(0xa0230000)
    data format: 64bits unsigned interger. Microseconds of the epoch time.
### IIo sensor
CPU:/sys/bus/iio/devices/iio\:device0
Power Current Sensor:/sys/bus/iio/devices/iio\:device1
### pdma
It is a user interface to transfer a DAM address of the user space to the physical address.
Device: /dev/pdma0
ioctl cmd: 0
ioctl parameters: struct{guint64 param_in; guint64 param_out}
param_in: the dma user-space address.
param_out: the dma physical address
### Reserve memory
reserve memory physcial address:0x70000000
reserve memory size: 0xff00000
### Watchdog
Device: /dev/watchdog0, /dev/watchdog1
watchdog0 is controlled by OS.
Watchdog1 can be controoled by the user.
# Programming
## A simple firmware
### Edit
Install Atom as the SDK editor. Install Atom requirement plugin.
Create the Project Folder and Add this project folder into the Atom.
create a new file ‘Makefile’ and a folder ‘src’ in this project folder.
Create a source file ‘main.c’ in the folder ‘src’.
edit Makefile:

TARGET := $(notdir $(CURDIR))
CSOURCES := $(wildcard src/*.c)
COBJECTS := $(CSOURCES:%.c=%.o)
CPPSOURCES := $(wildcard src/*.cpp)
CPPOBJECTS := $(CPPSOURCES:%.cpp=%.o)

CFLAGS := -O
LDFLAGS :=
LIBS :=

.PHONY: $(TARGET)

$(TARGET): $(COBJECTS) $(CPPOBJECTS)
$(CXX) -o $@ $^ $(LDFLAGS) $(LIBS)

$(COBJECTS): %.o: %.c
$(CC) $(CFLAGS) -o $@ -c $<

$(CPPOBJECTS): %.o: %.cpp
$(CXX) $(CFLAGS) -o $@ -c $<

clean:
rm -rf *~ .dep $(COBJECTS) $(CPPOBJECTS) $(TARGET)

edit the main.c:
#include <stdio.h>

int main()
{
printf(“hello world!\n”);
return 0;
}

### Compile
Open Terminal and Go to your project folder. Run “make”.
Then you get a executable file ‘<your-project-folder>’ in <your-project-folder>.
### Run firmware
- Download the executable file to /usr/local/bin in the VCU with the sftp client software
- Open GTKTerm and connect to the VCU with the USB debug port.(e.g /dev/ttyUSB0)
- Disable the original VCU firmware in /etc/init.d/loaduserapp.sh and reboot the VCU
- go to the folder /usr/local/bin and run your application