SDK and system resources of B3VDU

Revision History
Name	Date	Reason For Changes	Version
Chen Yong	Jul 8, 2022	Initial draft	1.0.1

# Scope
# System

VDU
VCU
Programming
computer
RS422

USB Debug Serial Port

Ethernet

Sdi input

Figure is the full system physical linking. The devices and linking for programming are in the dotted line box.

# Enviroment
## VDU
Defaut setting:
static IP (192.168.9.115)
- username: root
- password: root
The user can download and upload files to VDU with sftp client software.
The user can control the VDU with the serial port debug application(e.g: teraterm).
The user also can log in and control the VDU with putty or ssh.
## Programming computer
- This computer is for programming the software fo the VDU. The Ubuntu(20.04) is required and verified to work.
- This computer has the same subnet IP address with the VDU.
- The user need install the requirement software eg Filezilla(sftp client), GTKTerm(serial debug) or ssh for downloading, uploading and debugging the VDU files.
- The user run sdk.sh(from teamone) to install the sdk compiler.
- <your-sdk-dir>/environment-setup-cortexa72-cortexa53-xilinx-linux includes the enviroment setup for the compiler. The user need setup the enviroment of the compiler based on their SDK requirement.
# B3VDU system resources
## External interface
### LCD
.LVDS: LCD video data signal.
.LCD DIM PWM output: adjust LCD bright.
output control reference 4.2.2
### UART
This port is link to the VCU for the VDU switching command.
Format: TIA/EIA-422
Device name: /dev/ttyS1
working mode:Duplex
flow control: no
### Ethernet
10/100/1000 BASE-T
ifname: eth0
### KeyPad
Key No	Gpio port	Key name	Linux code
KEY_DIN_1	<axi_gpio_0 0>	key1	KEY_1(2)	FRONT
KEY_DIN_2	<axi_gpio_0 1>	key2	KEY_2(3)	REAR
KEY_DIN_3	<axi_gpio_0 2>	key3	KEY_3(4)	IR
KEY_DIN_4	<axi_gpio_0 3>	key4	KEY_4(5)	NUC
KEY_DIN_5	<axi_gpio_0 4>	key5	KEY_5(6)	NIGHT
KEY_DIN_6	<axi_gpio_0 5>	key6	KEY_6(7)	MINUS
KEY_DIN_7	<axi_gpio_0 6>	key7	KEY_7(8)	PLUS
KEY_DIN_8	<axi_gpio_0 7>	key8	KEY_8(9)	MENU

### SDI Input
control reference 4.2.2
### CAN
Ifname: can0
Spare device
## Internal Interface
### I2C
device name: /dev/i2c-0
slave chip: mb85rc256vfp slave address: 0x50
description: log data storage
### video registers
Registers Physical address: 0xa0000000
Registers Physical size: 0x2000
Registers data: 32bits
registers	W/R	items	value
0x0000	W/R	brightness	0 - 100
0x0004	W/R	NVG brightness	0 - 100 / default 10
0x0008	W/R	NVG mode	0 – normal mode / 1 – NVG mode
0x000C	W/R	auto_manu	0 – auto select video / 1 – manual select video
0x0010	W/R	osdCtrl	0 – no OSD / 1 – overlay OSD
0x0014	W/R	video source	0 – video source 0 / 1 - video source 1
0x0018	W/R	contrast value	0 – 100 convert to -255 ~ 255 / (x- 50) x 255 /50
0x001C	W/R	color value	0 – 100 convert to -255 ~ 255 / (x- 50) x 255 /50
0x0100	read only	status	bit 3-0 -- sdi 4 inputs: 0 normal, 1 no signal / bit 4 -- ddr read: 0 normal, 1 no read operation / bit 5 -- ddr write: 0 normal, 1 no write operation / bit 7-6 – display: 00 normal, 01 no signal, 10 error

### OSD memory
Osd physcial address: 0x70000000
Osd Resolution: 1920x1080
Osd format: RGBA32
### iio sensor
CPU:/sys/bus/iio/devices/iio\:device0
Power Current Sensor:/sys/bus/iio/devices/iio\:device1
### Watchdog
Device: /dev/watchdog0, /dev/watchdog1
watchdog0 is controlled by OS.
Watchdog1 can be controoled by the user.
# Programming
## A simple firmware
### Edit
Install Atom as the SDK editor. Install Atom requirement plugin.
Create the Project Folder and Add this project folder into the Atom.
create a new file ‘Makefile’ and a folder ‘src’ in this project folder.
Create a source file ‘main.c’ in the folder ‘src’.
edit Makefile:

TARGET := $(notdir $(CURDIR))
CSOURCES := $(wildcard src/*.c)
COBJECTS := $(CSOURCES:%.c=%.o)
CPPSOURCES := $(wildcard src/*.cpp)
CPPOBJECTS := $(CPPSOURCES:%.cpp=%.o)

CFLAGS := -O
LDFLAGS :=
LIBS :=

.PHONY: $(TARGET)

$(TARGET): $(COBJECTS) $(CPPOBJECTS)
$(CXX) -o $@ $^ $(LDFLAGS) $(LIBS)

$(COBJECTS): %.o: %.c
$(CC) $(CFLAGS) -o $@ -c $<

$(CPPOBJECTS): %.o: %.cpp
$(CXX) $(CFLAGS) -o $@ -c $<

clean:
rm -rf *~ .dep $(COBJECTS) $(CPPOBJECTS) $(TARGET)

edit the main.c:
#include <stdio.h>

int main()
{
printf(“hello world!\n”);
return 0;
}

### Compile
Open Terminal and Go to your project folder. Run “make”.
Then you get a executable file ‘<your-project-folder>’ in <your-project-folder>.
### Run firmware
- Download the executable file to /usr/local/bin in the VDU with the sftp client software
- Open GTKTerm and connect to the VDU with the USB debug port.(e.g /dev/ttyUSB0)
- Disable the original VDU firmware in /etc/init.d/loaduserapp.sh and reboot the VDU
- go to the folder /usr/local/bin and run your application