B3VDU software resource specification

Revision History
Name	Date	Reason For Changes	Version
Chen Yong	Jan 14, 2022	Initial draft	1.0.1

# Scope
## Identification

## System overview

## Document overview
Chapter 1: Scope
Chapter 2: Referenced documents
Chapter 3: Requirements
Chapter 4: Requirements traceability
Chapter 5: Notes
chapter 6: Appendixes.
# Referenced documents
# Requirements
## Required states and modes
## CSCI capability requirements
## CSCI external interface requirements
### USB3.0
### LCD
.lvds
.(LCD DIM) PWM output
.(LED DIM) PWM output
output control reference (lvds: 3.4.2 lcd dim:3.4.3 led dim:3.4.4)
### UART
Format: RS422
Device name: /dev/ttyS1
working mode:Duplex
data: 115200n8
flow control: no
### Ethernet
10/100/1000 BASE-T
### KeyPad
Interface: axi_gpio_0 (0xa0130000)
Key No	Gpio port	Key name	Linux code
KEY_DIN_1	<axi_gpio_0 0>	key1	KEY_1(2)	FRONT
KEY_DIN_2	<axi_gpio_0 1>	key2	KEY_2(3)	REAR
KEY_DIN_3	<axi_gpio_0 2>	key3	KEY_3(4)	IR
KEY_DIN_4	<axi_gpio_0 3>	key4	KEY_4(5)	NUC
KEY_DIN_5	<axi_gpio_0 4>	key5	KEY_5(6)	NIGHT
KEY_DIN_6	<axi_gpio_0 5>	key6	KEY_6(7)	MINUS
KEY_DIN_7	<axi_gpio_0 6>	key7	KEY_7(8)	PLUS
KEY_DIN_8	<axi_gpio_0 7>	key8	KEY_8(9)	MENU

### SDI Input
Device name: /dev/media0 (/dev/video0) && /dev/media1 (/dev/video1)
support format: 1080P60 or lower resolution.
### CAN
## CSCI internal interface requirements
### I2C
device name: /dev/i2c-0
slave chip: mb85rc256vfp slave address: 0x50
description: log data storage
### v_mix_0(0xb0010000)
device name: v_mix_0
primary stream(Video): plane=37 format=BG24
2nd stream(sdi): plane=34 format=XV20
3rd stream(h264/h265): plane35 format=NV12
4th stream(OSD): plane=36 format=AR24
### axi_timer_0
device: xilinx axi timer.(PWM mode)
Phy Address:0xa0140000
Desciption:LCD DIM
### axi_timer_1
device: xilinx axi timer(PWM mode)
phy address:0xa0150000
description: LED DIM
### iio sensor
CPU:/sys/bus/iio/devices/iio\:device0
Power Current Sensor:/sys/bus/iio/devices/iio\:device1
## CSCI internal data requirements
PGParam (glb_priv_data_t)	Sysbits (guint32)	Bit0: memory / bit1: logdata / bit2: snsor / bit3: current / bit4: temperature / bit5: pwm0 / bit6: pwm1 / bit7: keypad / bit8: video out / bit9: video in0 / bit10: video in1 / bit11: osd / bit12: serial / bit13: host	System BIT information: / 0: pass / 1: fail

# Requirements traceability
# Note
# Appendixes
## Version Log
Vesrion	Date	content
1.0.1	30 Jun 2022	initial version
1.0.2	14 Jul 2022	add "NUC mode" in menu add "NUC mode" bit in sending key package based on STK document "VDU View Switching 13072022.pptx"
1.0.3	11 Aug 2022	Modify OSD based on STK document "VDU View Switching 25072022.pptx"
1.0.4	17 Aug 2022	Modify OSD based on STK document "VDU Software V0.5_16082022.pptx"
1.0.5	20 Sep 2022	insert "VDU software Version", "Reset to Default" item into menu. the lowest contrast value is 10. based on STK doucunent "VDU Software V0.6_20092022.pptx"
1.0.6	1 Nov 2022	change RS422 protocol (move "elapsetime" from "DEV" package to "KEY" package) based on STK document "VCU_IDS_V0.4.xlsx"
2.0.1	15 Nov 2022	rebuild system by Petalinux 2022.2 Add Font into system. Add brightness value under brightness bar base on "VDU Software V0.7_31102022.pptx"
2.0.2	8 Feb 2023	Change NUC protocol base on "VDU Software V0.8_0602023.pptx"